## Slide 1: Binary Adder/Subtractor

## Slide 2: 4-bit Binary Adder
This is also called Ripple Carry Adder ,
because of the construction with full adders
are connected in cascade.
4-bit Binary Adder

## Slide 3: 4-bit BinaryAdder/Subtractor with overflow
M = 1subtractor ; M = 0adder

## Slide 4
Full-adder can also implemented with two half adders and one OR gate.
S = z ⊕ (x ⊕ y)
= z’(xy’ + x’y) + z(xy’ + x’y)’
= xy’z’ + x’yz’ + xyz + x’y’z
C = z(xy’ + x’y) + xy = xy’z + x’yz + xy
Full adder using half adder

## Slide 5: Boolean functions for Carry look ahead adder
Pi = Ai ⊕ Bi steady state value
Gi = AiBi steady state value
Output sum and carry
Si = Pi ⊕ Ci
Ci+1 = Gi + PiCi
Gi : carry generate Pi : carry propagate
C0 = input carry
C1 = G0 + P0C0
C2 = G1 + P1C1 = G1 + P1G0 + P1P0C0
C3 = G2 + P2C2 = G2 + P2G1 + P2P1G0 + P2P1P0C0
C3 does not have to wait for C2 and C1 to propagate.

## Slide 6: Logic diagram of carry look-ahead generator
C3 is propagated at the same time as C2 and C1.

## Slide 7: 4-bit adder with carry look ahead
Delay time of n-bit CLAA = XOR + (AND + OR) + XOR

## Slide 8: Thank You