## Slide 1: Carry Look Ahead Adder

## Slide 2: Carry Look Ahead Adder
Binary adder causes a unstable factor on carry bit, and produces a longest propagation delay.
The signal from Ci to the output carry Ci+1, propagates through an AND and OR gates, so, for an n-bit RCA, there are 2n gate levels for the carry to propagate from input to output.
Because the propagation delay will affect the output signals on different time, so the signals are given enough time to get the precise and stable outputs.
The most widely used technique employs the principle of carry look-ahead to improve the speed of the algorithm.
No Carry
Carry Generate
Carry Propagate

## Slide 3
Pi = Ai ⊕ Bi steady state value
Gi = AiBi steady state value
Output sum and carry
Si = Pi ⊕ Ci
Ci+1 = Gi + PiCi
Gi : carry generate Pi : carry propagate
C0 = input carry
C1 = G0 + P0C0
C2 = G1 + P1C1 = G1 + P1G0 + P1P0C0
C3 = G2 + P2C2 = G2 + P2G1 + P2P1G0 + P2P1P0C0
C3 does not have to wait for C2 and C1 to propagate.

## Slide 4
4-bit Carry Look Ahead Adder

## Slide 5: Thank You