## Slide 1: CENTRAL PROCESSING UNIT
  Introduction
  General Register Organization
  Stack Organization
  Instruction Formats
  Addressing Modes
  Data Transfer and Manipulation
  Program Control
  Reduced Instruction Set Computer (RISC)

## Slide 2: Components of CPU

## Slide 3: GENERAL REGISTER ORGANIZATION
MUX
SELA
{
MUX
}
SELB
ALU
OPR
R1
R2
R3
R4
R5
R6
R7
Input
3 x 8
decoder
SELD
Load
(7 lines)
Output
A bus
B bus
Clock

## Slide 4: OPERATION OF CONTROL UNIT
The control unit directs the information flow through ALU by:
- Selecting various Components in the system
- Selecting the Function of ALU
Example: R1 <- R2 + R3
[1] MUX A selector (SELA): BUS A  R2
[2] MUX B selector (SELB): BUS B  R3
[3] ALU operation selector (OPR): ALU to ADD
[4] Decoder destination selector (SELD): R1  Out Bus
Control Word
Encoding of register selection fields
  Binary
  Code SELA SELB SELD
  000 Input Input None
  001 R1 R1 R1
  010 R2 R2 R2
  011 R3 R3 R3
  100 R4 R4 R4
  101 R5 R5 R5
  110 R6 R6 R6
  111 R7 R7 R7
SELA
SELB
SELD
OPR
3
3
3
5

## Slide 5: ALU CONTROL
Encoding of ALU operations
OPR
Select Operation Symbol
00000 Transfer A TSFA
00001 Increment A INCA
00010 ADD A + B ADD
00101 Subtract A - B SUB
00110 Decrement A DECA
01000 AND A and B AND
01010 OR A and B OR
01100 XOR A and B XOR
01110 Complement A COMA
10000 Shift right A SHRA
11000 Shift left A SHLA
Examples of ALU Microoperations
Symbolic Designation
Microoperation SELA SELB SELD OPR Control Word
Control
  R1  R2 - R3 R2 R3 R1 SUB 010 011 001 00101
  R4  R4  R5 R4 R5 R4 OR 100 101 100 01010
  R6  R6 + 1 R6 - R6 INCA 110 000 110 00001
  R7  R1 R1 - R7 TSFA 001 000 111 00000
  Output  R2 R2 - None TSFA 010 000 000 00000
  Output  Input Input - None TSFA 000 000 000 00000
  R4  shl R4 R4 - R4 SHLA 100 000 100 11000
  R5  0 R5 R5 R5 XOR 101 101 101 01100

## Slide 6: ALU CONTROL
Encoding of ALU operations
OPR
Select Operation Symbol
00000 Transfer A TSFA
00001 Increment A INCA
00010 ADD A + B ADD
00101 Subtract A - B SUB
00110 Decrement A DECA
01000 AND A and B AND
01010 OR A and B OR
01100 XOR A and B XOR
01110 Complement A COMA
10000 Shift right A SHRA
11000 Shift left A SHLA
Examples of ALU Microoperations
Symbolic Designation
Microoperation SELA SELB SELD OPR Control Word
Control
  R1  R2 + R3
  R4  R4
  R5  R5 - 1
  R6  Shl R1
  R7  Input

## Slide 7: ALU CONTROL
Encoding of ALU operations
OPR
Select Operation Symbol
00000 Transfer A TSFA
00001 Increment A INCA
00010 ADD A + B ADD
00101 Subtract A - B SUB
00110 Decrement A DECA
01000 AND A and B AND
01010 OR A and B OR
01100 XOR A and B XOR
01110 Complement A COMA
10000 Shift right A SHRA
11000 Shift left A SHLA
Examples of ALU Microoperations
Symbolic Designation
Microoperation SELA SELB SELD OPR Control Word
Control
  R1  R2 + R3 R2 R3 R1 ADD
  R4  R4 R4 - R4 TSFA
  R5  R5 - 1 R5 - R5 DECA
  R7  R1 R1 - R7 TSFA
  Output  R2 R2 - None TSFA