## Slide 1: STACK ORGANIZATION
Register Stack
Push, Pop operations
/* Initially, SP = 0, EMPTY = 1, FULL = 0 */
PUSH
POP
  SP  SP + 1 DR  M[SP]
  M[SP]  DR SP  SP - 1
  If (SP = 0) then (FULL  1) If (SP = 0) then (EMPTY  1)
  EMPTY  0 FULL  0
Stack
- Efficient for arithmetic expression evaluation
- Storage which can be accessed in LIFO
- Pointer: SP
- Only PUSH and POP operations are applicable
A
B
C
0
1
2
3
4
63
Address
FULL
EMPTY
SP
DR
Flags
Stack pointer
stack

## Slide 2: MEMORY STACK ORGANIZATION
- A portion of memory is used as a stack with a
processor register as a stack pointer
- PUSH: SP  SP - 1
  M[SP]  DR
- POP: DR  M[SP]
  SP  SP + 1
Memory with Program, Data,
and Stack Segments
DR
4001
4000
3999
3998
3997
3000
Data
(operands)
Program
(instructions)
1000
PC
AR
SP
stack

## Slide 3: REVERSE POLISH NOTATION
A + B Infix notation
+ A B Prefix or Polish notation
A B + Postfix or reverse Polish notation
- The reverse Polish notation is very suitable for stack manipulation
Evaluation of Arithmetic Expressions
Any arithmetic expression can be expressed in parenthesis-free
Polish notation, including reverse Polish notation
(3 * 4) + (5 * 6)  3 4 * 5 6 * +
Arithmetic Expressions: A + B
3
3
12
12
12
12
42
4
5
5
6
30
3
4
*
5
6
*
+

## Slide 4
Let SP=000000 in Fig1, then how many items are there in the stack if FULL=1 & EMTY=0 & FULL=0 & EMTY=1.
A stack is organized such that SP can be initialized to 4000 in Fig. 2 and the first item in the stack is stored at location 4000. List the micro-operation for PUSH and POP operation.
Convert the following arithmetic expressions in to reverse polish notation and show the stack operations for evaluating the numerical result:
(3+4) [10*(2+6)+8]