## Slide 1: INSTRUCTION FORMAT
OP-code field - specifies the operation to be performed
Address field - designates memory address(s) or a processor register(s)
Mode field - specifies the way the operand or the
effective address is determined
The number of address fields in the instruction format
depends on the internal organization of CPU
- The three most common CPU organizations:
Instruction Format
  Single accumulator organization:
  ADD X /* AC  AC + M[X] */
  General register organization:
  ADD R1, R2, R3 /* R1  R2 + R3 */
  ADD R1, R2 /* R1  R1 + R2 */
  MOV R1, R2 /* R1  R2 */
  ADD R1, X /* R1  R1 + M[X] */
  Stack organization:
  PUSH X /* TOS  M[X] */
  ADD
Instruction Fields

## Slide 2: THREE, and TWO-ADDRESS INSTRUCTIONS
Three-Address Instructions:
Program to evaluate X = (A + B) * (C + D) :
ADD R1, A, B /* R1  M[A] + M[B] */
ADD R2, C, D /* R2  M[C] + M[D] */
MUL X, R1, R2 /* M[X]  R1 * R2 */
- Results in short programs
- Instruction becomes long (many bits)
Two-Address Instructions:
Program to evaluate X = (A + B) * (C + D) :
MOV R1, A /* R1  M[A] */
ADD R1, B /* R1  R1 + M[B] */
MOV R2, C /* R2  M[C] */
ADD R2, D /* R2  R2 + M[D] */
MUL R1, R2 /* R1  R1 * R2 */
MOV X, R1 /* M[X]  R1 */

## Slide 3: ONE, and ZERO-ADDRESS INSTRUCTIONS
One-Address Instructions:
- Use an implied AC register for all data manipulation
- Program to evaluate X = (A + B) * (C + D) :
LOAD A /* AC  M[A] */
ADD B /* AC  AC + M[B] */
STORE T /* M[T]  AC */
LOAD C /* AC  M[C] */
ADD D /* AC  AC + M[D] */
MUL T /* AC  AC * M[T] */
STORE X /* M[X]  AC */
Zero-Address Instructions:
- Can be found in a stack-organized computer
- Program to evaluate X = (A + B) * (C + D) :
PUSH A /* TOS  A */
PUSH B /* TOS  B */
ADD /* TOS  (A + B) */
PUSH C /* TOS  C */
PUSH D /* TOS  D */
ADD /* TOS  (C + D) */
MUL /* TOS  (C + D) * (A + B) */
POP X /* M[X]  TOS */

## Slide 4
Question:
Write a program to evaluate the arithmetic statement by using Three, Two ,One and Zero address instruction.
a. A-B+(C+D)/E+F/G+(J*K)
b. (A*B+C)+D/E+F*G+I*J

## Slide 5: ADDRESSING MODES
Addressing Modes:
* Specifies a rule for interpreting or modifying the
address field of the instruction (before the operand
is actually referenced)
* Variety of addressing modes
- to give programming flexibility to the user
- to use the bits in the address field of the
instruction efficiently

## Slide 6: TYPES OF ADDRESSING MODES
Implied Mode
Address of the operands are specified implicitly
in the instruction
- No need to specify address in the instruction
- Ex: CMA(Complement the accumulator)
Immediate Mode
Instead of specifying the address of the operand,
the instruction contains the operand itself.
Direct Address Mode
Instruction specifies the memory address which
can be used directly to get the operand.
Indirect Addressing Mode
The address field of an instruction specifies the address of a memory location that contains the address of the operand.

## Slide 7: TYPES OF ADDRESSING MODES
Register Mode
Address specified in the instruction is the register address
Register Indirect Mode
Instruction specifies a register which contains the memory address of the operand
Auto-increment
Same as the Register Indirect, but when the address in the register is used to access memory, the value in the register is incremented after the execution of the instruction.
Auto-decrement features:
Same as the Register Indirect, but when the address in the register is used to access memory, the value in the register is decremented before the execution of the instruction.

## Slide 8: TYPES OF ADDRESSING MODES
Relative Addressing Modes
The Address fields of an instruction specifies the part of the address (abbreviated address) which can be used along with a PC to calculate the address of the operand
EA = PC + IR(address)
- Address field of the instruction is short
- Large physical memory can be accessed with a small number of address bits
Indexed Addressing Mode
XR: Index Register:
- EA = XR + IR(address)
Base Register Addressing Mode
BAR: Base Address Register:
- EA = BAR + IR(address)

## Slide 9: ADDRESSING MODES - EXAMPLES
Addressing
Mode
Effective
Address
Content
of AC
  Direct address
  Immediate operand
  Indirect address
  Relative address
  Indexed address
  Register
  Register indirect
  Autoincrement
  Autodecrement
Load to AC Mode
Address = 500
Next instruction
200
201
202
399
400
450
700
500
800
600
900
702
325
800
300
Memory
Address
PC = 200
R1 = 400
XR = 100
AC

## Slide 10: ADDRESSING MODES - EXAMPLES
Addressing
Mode
Effective
Address
Content
of AC
  Direct address 500 800
  Immediate operand 201 500
  Indirect address 800 300
  Relative address 702 325
  Indexed address 600 900
  Register - 400
  Register indirect 400 700
  Autoincrement 400 700
  Autodecrement 399 450
Load to AC Mode
Address = 500
Next instruction
200
201
202
399
400
450
700
500
800
600
900
702
325
800
300
Memory
Address
PC = 200
R1 = 400
XR = 100
AC

## Slide 11
A two-word instruction is stored in memory at an address designated by the symbol W. The address field of the instruction(stored at W+1) is designated by the symbol Y. The operand used during the execution of the instruction is stored at an address symbolized by Z. An index register contains the value X. State how Z is calculated from the other addresses if the addressing mode of the instruction is : Direct, Indirect, Relative, Indexed.
An instruction is stored at location 300 with its address field at location 301. The address field has the value 400. A processor register R1 contains the number 200. Evaluate the effective address if the addressing mode of the instruction is : direct, immediate, relative, register indirect, index with R1 as the index register.